## Slide 1
8085 MICROPROCESSOR

## Slide 2
CONTENTS
1. What is Microprocessor
2. Intel 8085 Microprocessor
3. The Block Diagram of 8085 Microprocessor
4. Functional units of 8085 Microprocessor

## Slide 3
WHAT IS MICROPROCESSOR?
A microprocessor is a computer processor which incorporates the functions of a computer's central processing unit (CPU) on a single integrated circuit (IC), or at most a few integrated circuits.
The Intel 8085 is an 8- bit microprocessor produced by Intel and introduced in 1976.

## Slide 4
It is a software-binary compatible with the more famous Intel 8080 with only two minor instructions added to support its added interrupt and serial input/output features.

## Slide 5
REGISTER SECTION
1. Temporary Register
2. General purpose register
3. Special purpose register

## Slide 6
TEMPORARY REGISTER
In 8085 microprocessor,there are three temporary 8 bit register. One is used during calculation to keep data temporarily and then move it to destination ,the other two ‘W’ and ‘Z’ temporary register are used to hold data/address temporarily during execution of some instruction.

## Slide 7
GENERAL PURPOSE REGISTER
B-C,D-E,H-L are the general purpose register.
This register can also be used to work in pairs to hold 16-bit data.
The H-L pairs works as a memory pointer.
A memory pointer holds the address of a particular memory location.

## Slide 8
SPECIAL PURPOSE REGISTER
1. Accumulator
2. Instruction Register and Decoder
3. Program Counter
4. Stack Pointer
5. Flag Register

## Slide 9
1. ACCUMULATOR
It is an 8 bit Register use to perform Arithmetic Logical Input and output Operation.
It is connected to the Internal Bus and ALU.

## Slide 10
2. INSTRUCTION REGISTER & DECODER
In computing, an instruction register (IR) is the part of a CPU's control unit that holds the instruction currently being executed or decoded.
There is an Instruction Decoder which Decodes the information’s present in the instruction register for further processing.

## Slide 11
3. PROGRAM COUNTER
A program counter is a register in a computer processor that contains the address (location) of the instruction being executed at the current time.